## Slide 1: Network Simulation Course
Computer Techniques Engineering Department
College of Engineering and Technology
Al-Mustaqbal University
BY
Dr. Muamer N. Mohammed

## Slide 2: Lecture 6
Addressing & IP Class

## Slide 3: IPv4 Address Classes
Class D Addresses
A Class D address begins with binary 1110 in the first octet.
First octet range 224 to 239.
Class D address can be used to represent a group of hosts called a host group, or multicast group.
Class E Addresses
First octet of an IP address begins with 1111
First octet range 240 to 255.
Class E addresses are reserved for experimental purposes and should not be
used for addressing hosts or multicast groups.

## Slide 4: IP Addresses as Decimal Numbers ip=w.x.y.z

## Slide 5: Network IDs and Broadcast Addresses
An IP address such as 176.10.255.255 that has all binary 1s in the host bit positions is reserved for the broadcast address.
An IP address such as 176.10.0.0 that has all binary 0s in the host bit positions is reserved for the network address.

## Slide 6: IP ADDRESSING
7 Application
6 Presentation
5 Session
4 Transport
1 Physical
2 Data Link
3 Network
Format
x x x x x x x x . x x x x x x x x . x x x x x x x x . x x x x x x x x
where x is either 0 or 1
Example 1:
1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1 . 0 0 0 0 0 0 0 0 . 0 0 0 0 0 0 0 0
255.255.0.0
Example 2:
1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1 . 1 0 0 0 0 0 0 0 . 0 0 0 0 0 0 0 0
255.255.192.0

## Slide 7: IP ADDRESSING
7 Application
6 Presentation
5 Session
4 Transport
1 Physical
2 Data Link
3 Network
Network Address
Example 1:
IP address of computer 180.100.7.1
Mask
Network address
255.255.0.0
180.100.0.0
Example 2:
IP address of computer 180.100.7.1
Mask
Network address
255.255.255.0
180.100.7.0
Example 3:
IP address of computer 180.100.7.2
Mask
Network address
255.255.192.0
180.100.0.0

## Slide 8: IP ADDRESSING
7 Application
6 Presentation
5 Session
4 Transport
1 Physical
2 Data Link
3 Network
Mask
Valid mask are contiguous 1’s from left to right.
Examples:
Valid
255.0.0.0
255.255.0.0
255.255.255.0
Invalid
255.1.0.0
255.0.255.0
255.255.64.0
200.255.0.0

## Slide 9: IP addressing
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
allocates addresses
manages DNS
assigns domain names, resolves disputes

## Slide 10: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip-
>properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 11: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block | 11001000 00010111 00010000 00000000 |  | 200.23.16.0/20
Organization 0 | 11001000 00010111 00010000 | 00000000 | 200.23.16.0/23
Organization 1 | 11001000 00010111 00010010 | 00000000 | 200.23.18.0/23
Organization 2 | 11001000 00010111 00010100 | 00000000 | 200.23.20.0/23
... | ….. | …. | ….
Organization 7 | 11001000 00010111 00011110 | 00000000 | 200.23.30.0/23

## Slide 12: End of Lecture