## Slide 1
الوقاية من الاشعاع
Radiation Protection
AL-Mustaqbal University College
Department of Medical Physics
The fourth Stage
كلية المستقبل الجامعة
المرحلة الرابعة
قسم الفيزياء الطبية
LECTURE FOUR :
Units of Radiation Protection
Aaat. prof . Dr Forat Hamzah Dr. Ameen Alwan
1
4

## Slide 2
One - Rad (radiation absorbed dose)
Radiation Units
Units of Radiation Protection
Two - Rem (Roentgen equivalent man)
Three - Gray (Gy)
Four - Sievert (Sv)
Five - Curie (Ci)
Six - Becquerel (Bq)
Seven - Disintegrations per second (dps)
راد
ريم
جراي
سفرت
كوري
بيكريل
التفكك في الثانية

## Slide 3
راد (الجرعة الممتصة من الإشعاع)
Rad Unit
1 - Rad is a unit of absorbed dose of radiation.
2 - Rad unit is a measure of the amount of energy deposited in tissue
4 - Rad unit can be used for any type of radiation
5- Rad unit dose not describe the biological effects on the human body of the different radiations due
Radiation weighting factor (Q) : is a factor used to determine the equivalent absorbed dose from the absorbed dose averaged over a tissue or organ based on the type of radiation absorbed
One - Rad (radiation absorbed dose)
3- Rad unit represents the absorption of 100 ergs for each gram.
( The erg is a unit of energy equal to 10−7 joule )
to the weighting factor of radiation type Q.
عامل ترجيح الإشعاع
Dose : it is a quantity of a radiation or drug taken or recommended to be taken at one time
الجرعة
Rad = 100 ergs / g
erg = 10−7 joule / g
الراد هو وحدة الجرعة الممتصة من الإشعاع.
إرج
هي مقياس لكمية الطاقة المترسبة في الأنسجة
يمكن استخدام وحدة الراد لأي نوع من الإشعاع
وحدة الراد لا تصف الآثار البيولوجية
الجرعة الممتصة المكافئة

## Slide 4
Unit Rem
1- Rem unit is used to measure biological effects on the human body.
2- Rem is a unit that measures the low levels of different types of ionizing radiation.
3- .Rem is a unit of equivalent absorbed dose of radiation which takes into account the biological effects.
4- The dose in rem equals the dose in rad multiplied by the quality factor (Q).
Quality Factor (Q): It is a factor used in radiation protection to weight the absorbed dose.
rem = rad Q
Two - Rem (Roentgen equivalent man)
For Beta and Gamma radiation , the Q = 1 So, the rem = rad
For Alpha radiation , the Q = 20 So, the rem = 20 rad
Examples
وحدة الريم
تستخدم لقياس الآثار البيولوجية على جسم الإنسان
الجرعة الممتصة المكافئة
تستخدم لقياس الستويات المنخفضة من الطاقة
عامل الجودة

## Slide 5
Gray (Gy)
1- Gray unit represents the measured absorbed dose from exposure to radiation.
2- Gray is a measure of energy deposition in tissue.
3- A dose of one Gy is equivalent to a unit of energy (joule) deposited in a kilogram of material.
4- A Gray unit of absorbed radiation dose equal to 100 rad.
1 Gy = 100 rad = 1 joule/kg
Three - Gray (Gy)
Rad Unit
جراي

## Slide 6
Rad = 100 ergs / g
rem = rad Q
1 Gy = 100 rad = 1 joule/kg
erg = 10−7 joule / g

## Slide 7
It represents the biological effects of low levels of ionizing radiation on the human body.
It represents the probability of radiation-induced cancer and genetic damage.
Sievert (Sv): It is unit used to measure dose quantities of radiation such as ;
(i) Equivalent dose
(ii) Effective dose.
الجرعة المكافئة
الجرعة الفعالة
Effective dose
Four - Sievert (Sv)
Equivalent dose
It is a dose quantity in the International Commission on Radiological Protection (ICRP) system of radiological protection
سفرت
احتمالية الاصابة بالامراض منها السرطان والاضرار الجينية
يمثل المستويات المنخفضة للتاثيرات البايولوجية
هو كمية الجرعة حسب مقياس الوقاية الاشعاعية الدولية
كميات الجرعة من الإشعاع

## Slide 8
Five - Curie (Ci)
1- Curie (Ci) is traditional unit of radioactivity.
2- Curie is unit used to measure the number of decays per second.
3- Curie is equal to the radioactivity of one gram (1g) of pure radium-226.
Six - Becquerel (Bq)
The standard international unit of radioactivity equal to one decay per second.
Seven - Disintegrations per second (dps)
Disintegrations per second (dps) : The unit represents the number of subatomic particles ( alpha particles & alfa partical) or photons (gamma rays) which released from the nucleus of a given atom over one second.
One dps = 60 dpm(disintegrations per minute)
1 Becquerel (Bq) = 27 Picocurie (pCi)
كوري
بيكريل
هو الوحدة التقليدية لقياس النشاط الاشعاعي
هو وحد قياس عدد الامضحلال او التحلل لكل ثانية
يمثل النشاط الاشعاعي لغرام واحد للرادوم النقي 226
هو وحدة قياس النشاط الاشعاعي التي تعادل تحلل واحد لكل ثانية
1 dps = 1 Bq
تمثل هذه الوحدة عدد الجسيمات أو الفوتونات التي تنطلق من ذرة معينة خلال ثانية واحدة
التفكك في الثانية

## Slide 9
Questions
1 - Choose the wrong sentence related to the Rad unit
A- It is a unit of absorbed dose of radiation
B- It is a measure of the amount of energy deposited in tissue
C- It is a unit used to describe the biological effects
D- It is unit can be used for any type of radiation
D
A
B
C
2 - Choose the correct sentences related to the Rem unit
A- It is a unit that measures the low levels of different types of ionizing radiation
B- It is used to measure biological effects
C- It is unit represents the measured absorbed dose
D- The dose in rem equals the dose in rad multiplied by the quality factor
D
A
B
C

## Slide 10
3 - Choose the wrong sentence related to the Equivalent dose
A- It represents the biological effects of low levels of ionizing radiation on the human body
B- It represents the probability of radiation-induced cancer and genetic damage
C- It is a dose quantity in the International Commission on Radiological Protection
A
B
C
Questions
4 - Answer with True (T) or False (F) of the following:
( If False (F), give the correct answer )
A- Curie (Ci) is traditional unit of radioactivity
B- Becquerel (Bq) is standard international unit of radioactivity equal to one decay per second