## Slide 1
Ultrasound Imaging
التصوير بالموجات فوق الصوتية
التصوير الطبي
Medical Imaging
LECTURE 7
السونار
Dr. Ameen Alwan Dr. Forat Hamzah

## Slide 2
Sound
Classification of the sound waves
Ultrasound imaging
Ultrasound imaging system components
How a ultrasound imaging system works ?
Ultrasound imaging system benefits & risks
(السونار)
Ultrasound Imaging
التصوير بالموجات فوق الصوتية

## Slide 3
(السونار)
Ultrasound Imaging
التصوير بالموجات فوق الصوتية
What is sound?
Sound is a form of energy, and it is formed when air molecules vibrate and move in a pattern called waves. In addition, the sound move through a transmission medium such as a gas, liquid or solid.
Air Molecules
Amplitude
(Capacity)
.
Wavelength
Calculate the length of the sound wave
طول الموجة الصوتية = سرعة الصوت / تردد الموجه
Hz
343 m/s
Decibel
f / c = λ
1224 km/h

## Slide 4
النطاق المسموع
النطاق التحت صوتي
النطاق فوق الصوتي
The audible range of dogs, cats....
Classification of the sound waves
(السونار)
Ultrasound Imaging
التصوير بالموجات فوق الصوتية
It is audible range of the human ear with frequencies in the range from 20 to 20,000 Hz.
Audible Sounds:
Infrasound:
It is the inaudible range of the human ear with a frequency of less than 20 Hz
Ultrasounds:
These are sound waves that are outside the human ear's senses with frequencies above 20,000 Hz.
Sound range
20 Hz
20,000 Hz
Audible Sounds
Infrasound
Ultrasounds
f

## Slide 5
Ultrasound imaging
It is a type of medical imaging for obtaining 3D images of the of human body
It uses ultrasounds range
Used to look at organs and structures inside the body, such as view the heart, blood vessel, blood flowing, liver, and other organs.
In addition, it is also used with checking process during the pregnancy.
(السونار)
Ultrasound Imaging
التصوير بالموجات فوق الصوتية
التصوير بالموجات فوق الصوتية

## Slide 6
(السونار)
Ultrasound Imaging
التصوير بالموجات فوق الصوتية
Ultrasound imaging system components
Ultrasound imaging system consists of the following parts :
Control unit containing a computer, display screen, and a transducer (probe) that is used to do the scanning.
The probe is a small hand-held device attached to the scanner by a cord (wire). Some exams may use different transducers (with different abilities) during a single exam
Ultrasound gel placed directly on the skin to allow the sound waves to travel from the probe to the body.
Storage unit
Printer

## Slide 7
(السونار)
Ultrasound Imaging
التصوير بالموجات فوق الصوتية
- High-frequency sound waves (Ultrasounds) are transmitted from the transducer (probe) through the gel into the body.
- Next , the probe collects the sounds that bounce back from the body and the computer, then uses those sound waves to create an image.
- The ultrasound image is visible on a video display screen that looks like a computer or television monitor.
- These images are created based on the following :
--------ultrasound signal capacity
------- ultrasound signal frequency
------- and time it takes for the ultrasound signal to return from the patient ​to the probe.
How a Ultrasound Imaging System Works ?

## Slide 8
Benefits
Ultrasound imaging system is easy-to-use and inexpensive.
Ultrasound imaging is safe and does not use any ionizing radiation.
Ultrasound scanning gives a clear picture of soft tissues that do not show up well on x-ray images.
Ultrasound is the preferred imaging modality for the diagnosis and monitoring of pregnant women.
Risks
For ultrasound imaging, there are no known harmful effects on humans.
(السونار)
Ultrasound Imaging
التصوير بالموجات فوق الصوتية
Ultrasound imaging system benefits & risks